## Slide 1: UM EECS 270 F25 Introduction to Logic Design
13. Sequential Design Examples

## Slide 2: Sequence Detector in Verilog
State Table |  |  | 
S | in |  | out
 | 0 | 1 | 
zero1s | zero1s | one1 | 0
one1 | zero1s | two1s | 0
two1s | zero1s | three1s | 0
three1s | zero1s | three1s | 1
 | S+ |  | 
Transition List |  |  | 
S | Transition Expression | S+ | out
zero1s | ~in | zero1s | 0
zero1s | in | one1 | 0
one1 | ~in | zero1s | 0
one1 | in | two1s | 0
two1s | ~in | zero1s | 0
two1s | in | three1s | 0
three1s | ~in | zero1s | 1
three1s | in | three1s | 1
Transition Table |  |  | 
Q1 Q0 | in |  | out
 | 0 | 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
 | Q1+ Q0+ |  | 
State Assignment | 
parameter zero1s parameter one1 parameter two1s parameter three1s | = 2’b00; = 2'b01; = 2'b10; = 2'b11;

## Slide 3: Sequence Detector V1: assign
module SequenceDetectorV1(input clk, in, output out);
reg [1:0] Q; initial Q = 2'b00;
// Next-state logic: assign wire [1:0] D; assign D[1] = in & (Q[1] | Q[0]); assign D[0] = in & (Q[1] | ~Q[0]); // State Update always @(posedge clk) Q <= D;
// Output logic assign out = (Q[1] & Q[0]);
endmodule
Transition Table |  |  | 
Q1 Q0 | in |  | out
 | 0 | 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
 | Q1+ Q0+ |  | 

## Slide 4: Sequence Detector V1: always
module SequenceDetectorV1(input clk, in, output out);
reg [1:0] Q; initial Q = 2'b00;
// Next-state logic: always reg [1:0] D;
always @*
begin
D[1] <= in & (Q[1] | Q[0]);
D[0] <= in & (Q[1] | ~Q[0]);
end
// State Update always @(posedge clk) Q <= D;
// Output logic assign out = (Q[1] & Q[0]);
endmodule
Transition Table |  |  | 
Q1 Q0 | in |  | out
 | 0 | 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
 | Q1+ Q0+ |  | 

## Slide 5: Sequence Detector V2
module SequenceDetectorV2(input clk, in, output out); reg [1:0] Q, D; initial Q = 2'b00;
// State Transitions always @* begin case(Q) zero1s: if (in) D <= one1; else D <= zero1s; one1: if (in) D <= two1s; else D <= zero1s; two1s: if (in) D <= three1s; else D <= zero1s; three1s: if (in) D <= three1s; else D <= zero1s; endcase
end // State Update always @(posedge clk) Q <= D;
// Output logic assign out = (Q[1] & Q[0]);
endmodule
Transition List |  |  | 
S | Transition Expression | S+ | out
zero1s | ~in | zero1s | 0
zero1s | in | one1 | 0
one1 | ~in | zero1s | 0
one1 | in | two1s | 0
two1s | ~in | zero1s | 0
two1s | in | three1s | 0
three1s | ~in | zero1s | 1
three1s | in | three1s | 1

## Slide 6
ModelSim Demo

## Slide 7
Design a sequential circuit that monitors the condition of a patient in a hospital bed. The input to the circuit is a binary number n that ranges in value from 1 to 7 and indicates the patient’s condition. The expected value of n is 3, but values of 2 and 4 are not considered abnormal. A new value of n is sent to the monitor automatically every 5 seconds. If n goes below 2 or above 4 on two or more occasions, the monitor should activate an alarm at a nurse’s station. The nurse responds by administering medication to the patient and resetting the monitor. Construct a suitable state table and corresponding transition table for this circuit.

## Slide 9
Design a single-input single-output sequential circuit that recognizes the 4-bit input sequence 1010 including overlaps.
For example,
input sequence 0 0 1 0 1 0 0 1 0 1 0 1 0 1 1 1 0
output sequence 0 0 0 0 0 1 0 0 0 0 1 0 1 0 0 0 0

## Slide 10
Design a sequential circuit that compares two unsigned n-bit numbers X=xn-1 xn-2 . . . x0 and Y=yn-1 yn-2 . . . y0 applied serially starting with their most significant bits. The circuit should have two outputs z1 and z2 that indicate the result of the comparison according to the code:
z2 z1
0 0 X = Y
0 1 X > Y
1 0 X < Y